## Slide 1
Chapter 1:
From Zero to One
Digital Design &
Computer Architecture
Sarah Harris & David Harris

## Slide 2
The Art of Managing Complexity
Number Systems
  Binary Numbers
  Hexadecimal Numbers
  Bits, Bytes, Nibbles
  Addition
  Signed Numbers
  Extension
Logic Gates
Logic Levels
CMOS Transistors
Transistor-Level Gate Design
Power Consumption
Chapter 1 :: Topics

## Slide 3
Chapter 1: From Zero to One
The Art of
Managing Complexity

## Slide 4
How do we design things that are too big to fit in one person’s head at once?
Abstraction
Discipline
The Three –y’s
  Hierarchy
  Modularity
  Regularity
The Art of Managing Complexity

## Slide 5
Hiding details when they aren’t important
Abstraction

## Slide 6
Intentionally restrict design choices
Example: Digital discipline
  Discrete voltages instead of continuous
  Simpler to design than analog circuits – can build more sophisticated systems
  Digital systems replacing analog predecessors: i.e., digital cameras, digital television, cell phones, CDs
Discipline

## Slide 7
Hierarchy
  A system divided into modules and submodules
Modularity
  Having well-defined functions and interfaces
Regularity
  Encouraging uniformity, so modules can be easily reused
The Three -y’s

## Slide 8
Famous early (1908) example of interchangeable parts.
  Most previous cars were hand-crafted
  by skilled tradesmen.
  Mass production on moving assembly
  lines greatly reduced cost.
Henry Ford:
  I will build a motor car for the great multitude. It will be large enough for the family, but small enough for the individual to run and care for. It will be constructed of the best materials, by the best men to be hired, after the simplest designs that modern engineering can devise. But it will be so low in price that no man making a good salary will be unable to own one – and enjoy with his family the blessing of hours of pleasure in God's great open spaces.
Example: Model T Ford
en.wikipedia.org/wiki/Ford_Model_T#/media/
File:1925_Ford_Model_T_touring.jpg

## Slide 9
Hierarchy
  Car has chassis, wheels, seats, engine.
  Engine has cylinders, spark plugs, exhaust, carburetor.
  Carburator has air intake, inlet needle, feed pipe, coupling nut.
Example: Model T Ford
https://en.wikipedia.org/wiki/Ford_Model_T_engine#/media/File:Pagé_1917_Model_T_Ford_Car_Figure_08.png
https://en.wikipedia.org/wiki/Ford_Model_T_engine#/media/File:Pagé_1917_Model_T_Ford_Car_Figure_14.png

## Slide 10
Modularity
  Function of coupling nut:
    Hold fuel line to intake elbow
    Prevent leaks
    Easily removable
  Interface of coupling nut:
    Standardized diameter, thread pitch, torque
Regularity
  Interchangeable parts
    Standard nut could be purchased from many suppliers
  “Any customer can have a car painted any color that he wants so long as it is black.” - Henry Ford
Example: Model T Ford

## Slide 11
Most physical variables are continuous
  Voltage on a wire
  Frequency of an oscillation
  Position of a mass
Digital abstraction considers discrete subset of values
The Digital Abstraction

## Slide 12
Designed by Charles Babbage from 1834 – 1871
Considered to be the first digital computer
Built from mechanical gears, where each gear represented a discrete value (0-9)
Babbage died before finishing it
The Analytical Engine
Notes: Babbage found errors in manually calculated tables “I wish to God these calculations had been executed by steam.”
Babbage kept changing designs before getting them working.
Precision components were too difficult to manufacture in the shops of the day.
British Government granted over 17,000 pounds (each worth a pound of silver at the time), a princely sum, before pulling plug.
Babbage died a bitter and broken man.
Two working engines were built from his plans in 1991 and are on display in the Computer History Museum and the Science Museum.

## Slide 13
Two discrete values:
  1’s and 0’s
  1, TRUE, HIGH
  0, FALSE, LOW
1 and 0: voltage levels, rotating gears, fluid levels, etc.
Digital circuits use voltage levels
  0: low voltage (GND)
  1: high voltage (VDD)
Bit: Binary digit
Digital Discipline: Binary Values

## Slide 14
Chapter 1: From Zero to One
Number Systems:
Binary Numbers

## Slide 15
Decimal numbers
Binary numbers
Number Systems
Decimal numbers in digital systems mean any base 10 numbers, not just those with a decimal point.

## Slide 16
Binary Decimal
0 0
1 1
10 2
11 3
4
5
…
Counting in Binary

## Slide 17
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Powers of Two
Handy to memorize

## Slide 18
Binary to decimal conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112
Number Conversion

## Slide 19
Two methods:
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
Decimal to Binary Conversion

## Slide 20
  5310
  Method 1: Find the largest power of 2 that fits, subtract and repeat
  5310 32×1
  53-32 = 21 16×1
  21-16 = 5 4×1
  5-4 = 1 1×1 = 1101012
Method 2: Repeatedly divide by 2, remainder goes in next most significant bit
  5310 = 53/2 = 26 R1
  26/2 = 13 R0
  13/2 = 6 R1
  6/2 = 3 R0
  3/2 = 1 R1
  1/2 = 0 R1 = 1101012
Decimal to Binary Conversion

## Slide 21
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Binary Values and Range
Notes: There are 10 kinds of people in this world: those who can count in binary and those who can’t.

## Slide 22
Chapter 1: From Zero to One
Number Systems:
Hexadecimal Numbers

## Slide 23
Hexadecimal Numbers
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 24
Base 16
Shorthand for binary
Hexadecimal Numbers

## Slide 25
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  162×4 + 161×10 + 160×15 = 119910
Hexadecimal to Binary Conversion

## Slide 26
Hard to write subscripts in text files
Some programming languages uses prefixes
  Hex: 0x
    0x23AB = 23AB16
  Binary: 0b
    0b1101 = 11012
Hexadecimal and Binary Prefixes

## Slide 27
Chapter 1: From Zero to One
Number Systems:
Bytes, Nibbles,
& All That Jazz

## Slide 28
Byte: 8 bits
  Represents one of _____ values
  [__, ___]
Nibble: 4 bits
  Represents one of _____ values
  [__, ___]
One binary digit is __ bit
One hex digit is ___ bits or ___ nibble
Two hex digits make ___ byte
Most significant on left
Least significant on right
Bits, Bytes, Nibbles…

## Slide 29
Large Powers of Two
210 = 1 kilo ≈ 103 (1024)
220 = 1 mega ≈ 106 (1,048,576)
230 = 1 giga ≈ 109 (1,073,741,824)
240 = 1 tera ≈ 1012
250 = 1 peta ≈ 1015
260 = 1 exa ≈ 1018

## Slide 30
What is the value of 224?
24 × 220 ≈ 16 million
How large of a value can a 32-bit integer variable represent?
22 × 230 ≈ 4 billion
Estimating Powers of Two

## Slide 31
Chapter 1: From Zero to One
Number Systems:
Addition

## Slide 32
Decimal
Binary
Addition

## Slide 33
Add the following 4-bit binary numbers
Add the following 4-bit binary numbers
Binary Addition Examples

## Slide 34
Digital systems operate on a fixed number of bits
Overflow: when result is too big to fit in the available number of bits
See previous example of 11 + 6
Overflow

## Slide 35
Chapter 1: From Zero to One
Number Systems:
Signed Numbers

## Slide 36
Sign/Magnitude Numbers
Two’s Complement Numbers
Signed Binary Numbers

## Slide 37
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign/mag representations of ± 6:
+6 = 0110
- 6 = 1110
Range of an N-bit sign/magnitude number:
[-(2N-1-1), 2N-1-1]
Sign/Magnitude Numbers

## Slide 38
Problems:
Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
Two representations of 0 (± 0):
1000
0000
Sign/Magnitude Numbers

## Slide 39
Don’t have same problems as sign/magnitude numbers:
  Addition works
  Single representation for 0
Two’s Complement Numbers

## Slide 40
msb has weight of -2N-1
Most positive 4-bit number: 0111
Most negative 4-bit number: 1000
The most significant bit still indicates the sign (1 = negative, 0 = positive)
  Range of an N-bit two’s complement number:
  [-(2N-1), 2N-1-1]
Two’s Complement Numbers
+

## Slide 41
Reverse the sign of a two’s complement number
Method:
    Invert the bits
    Add 1
Example: Reverse the sign of 310 = 00112
    1100
    + 1
    1101 = -310
Reversing the Sign
Historically, this reversing the sign method has been called: “Taking the Two’s complement”.
But this terminology can be confusing, so we instead we call it “reversing the sign”.

## Slide 42
Reverse the sign of 610 = 01102
    1001
    + 1
    10102 = -610
What is the decimal value of the two’s complement number 10012?
    0110
    + 1
    01112 = 710, so 10012 = -710
Two’s Complement Examples

## Slide 43
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers
Two’s Complement Addition

## Slide 44
Subtract a 2’s complement number by reversing the sign and adding.
Reverse sign by taking 2’s complement
Ex: 3 – 5 = 3 + (-5)
Subtraction

## Slide 45
Number System | Range
Unsigned | [0, 2N-1]
Sign/Magnitude | [-(2N-1-1), 2N-1-1]
Two’s Complement | [-2N-1, 2N-1-1]
For example, 4-bit representation:
Number System Comparison

## Slide 46
Chapter 1: From Zero to One
Number Systems:
Extension

## Slide 47
Extend number from N to M bits (M > N) :
  Sign-extension for 2’s complement numbers
  Zero-extension for unsigned numbers
Increasing Bit Width

## Slide 48
Sign bit copied to msb’s
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011
Sign-Extension

## Slide 49
Zeros copied to msb’s
Value changes for negative numbers
Example 1:
  4-bit value = 0011 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110
Zero-Extension

## Slide 50
Chapter 1: From Zero to One
Logic Gates

## Slide 51
Perform logic functions:
  inversion (NOT), AND, OR, NAND, NOR, etc.
Single-input:
  NOT gate, buffer
Two-input:
  AND, OR, XOR, NAND, NOR, XNOR
Multiple-input
Logic Gates

## Slide 52
Single-Input Logic Gates

## Slide 53
Two-Input Logic Gates

## Slide 54
More Two-Input Logic Gates

## Slide 55
Multiple-Input Logic Gates
Multi-input XOR: Odd parity
Truth table rows
are listed in
binary order.

## Slide 56
SystemVerilog Description
module gates(input logic a, b, c,
output logic y1, y2, y3, y4, y5);
not g1(y1, a);
and g2(y2, a, b);
or g3(y3, a, b, c);
nand g4(y4, b, c);
xor g5(y5, a, c);
endmodule

## Slide 57
Born to working class parents
Taught himself mathematics and joined the faculty of Queen’s College in Ireland
Wrote An Investigation of the Laws of Thought (1854)
Introduced binary variables
Introduced the three fundamental logic operations: AND, OR, and NOT
George Boole, 1815-1864

## Slide 58
Chapter 1: From Zero to One
Logic Levels

## Slide 59
Discrete voltages represent 1 and 0
For example:
  0 = ground (GND) or 0 volts
  1 = VDD or 5 volts
What about 4.99 volts? Is that a 0 or a 1?
What about 3.2 volts?
Logic Levels

## Slide 60
Range of voltages for 1 and 0
Different ranges for inputs and outputs to allow for noise
Logic Levels

## Slide 61
Anything that degrades the signal
  E.g., resistance, power supply noise, coupling to neighboring wires, etc.
Example: a gate (driver) outputs 5 V but, because of resistance in a long wire, receiver gets 4.5 V
What is Noise?

## Slide 62
With logically valid inputs, every circuit element must produce logically valid outputs
Use limited ranges of voltages to represent discrete values
The Static Discipline

## Slide 63
Noise Margins

## Slide 64
High Noise Margin: NMH = VOH – VIH
Low Noise Margin: NML = VIL – VOL
Noise Margins

## Slide 65
Ideal Buffer: Real Buffer:
NMH = NML = VDD/2
DC Transfer Characteristics
NMH, NML < VDD/2

## Slide 66
DC Transfer Characteristics

## Slide 67
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
  Be careful connecting chips with different supply voltages
VDD Scaling

## Slide 68
In 1970’s and 1980’s, VDD = 5 V
VDD has dropped
  Avoid frying tiny transistors
  Save power
3.3 V, 2.5 V, 1.8 V, 1.5 V, 1.2 V, 1.0 V, …
  Be careful connecting chips with different supply voltages
Chips operate because they contain magic smoke
Proof: if the magic smoke is let out, the chip stops working
VDD Scaling

## Slide 69
Logic Family | VDD | VIL | VIH | VOL | VOH
TTL | 5 (4.75 - 5.25) | 0.8 | 2.0 | 0.4 | 2.4
CMOS | 5 (4.5 - 6) | 1.35 | 3.15 | 0.33 | 3.84
LVTTL | 3.3 (3 - 3.6) | 0.8 | 2.0 | 0.4 | 2.4
LVCMOS | 3.3 (3 - 3.6) | 0.9 | 1.8 | 0.36 | 2.7
Logic Family Examples

## Slide 70
Chapter 1: From Zero to One
CMOS Transistors

## Slide 71
Logic gates built from transistors
3-ported voltage-controlled switch
  2 ports connected depending on voltage of 3rd
  d and s are connected (ON) when g is 1
Transistors

## Slide 72
Nicknamed “Mayor of Silicon Valley”
Cofounded Fairchild Semiconductor in 1957
Cofounded Intel in 1968
Co-invented the integrated circuit
Robert Noyce, 1927-1990

## Slide 73
Transistors built from silicon, a semiconductor
Pure silicon is a poor conductor (no free charges)
Doped silicon is a good conductor (free charges)
  n-type (free negative charges, electrons)
  p-type (free positive charges, holes)
Silicon

## Slide 74
Metal oxide silicon (MOS) transistors:
  Polysilicon (used to be metal) gate
  Oxide (silicon dioxide) insulator
  Doped silicon
MOS Transistors

## Slide 75
Gate = 0
OFF (no connection between source and drain)
Gate = 1
ON (channel between source and drain)
Transistors: nMOS

## Slide 76
pMOS transistor is opposite
  ON when Gate = 0
  OFF when Gate = 1
Transistors: pMOS

## Slide 77
Transistor Function

## Slide 78
nMOS: pass good 0’s, so connect source to GND
pMOS: pass good 1’s, so connect source to VDD
Transistor Function

## Slide 79
Chapter 1: From Zero to One
Gates from Transistors

## Slide 80
CMOS Gates: NOT Gate
A | P1 | N1 | Y
0 | ON | OFF | 1
1 | OFF | ON | 0

## Slide 81
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 1
1 | 0 | OFF | ON | ON | OFF | 1
1 | 1 | OFF | OFF | ON | ON | 0
CMOS Gates: NAND Gate

## Slide 82
CMOS Gate Structure

## Slide 83
NOR3 Gate
How do you build a three-input NOR gate?

## Slide 84
AND2 Gate
How do you build a two-input AND gate?

## Slide 85
nMOS pass 1’s poorly
pMOS pass 0’s poorly
Transmission gate is a better switch
  passes both 0 and 1 well
When EN = 1, the switch is ON:
  EN = 0 and A is connected to B
When EN = 0, the switch is OFF:
  A is not connected to B
Transmission Gates

## Slide 86
Cofounded Intel in 1968 with Robert Noyce.
Moore’s Law: number of transistors on a computer chip doubles every year (observed in 1965)
Since 1975, transistor counts have doubled every two years.
Corollaries: transistors get faster and lower power
Gordon Moore, 1929-

## Slide 87
“If the automobile had followed the same development cycle as the computer, a Rolls-Royce would today cost $100, get one million miles to the gallon, and explode once a year . . .” (Robert Cringely, Infoworld)
– Robert Cringley
Moore’s Law

## Slide 88
Chapter 1: From Zero to One
Power Consumption

## Slide 89
Power = Energy consumed per unit time
Dynamic power consumption
Static power consumption
Power Consumption

## Slide 90
Power to charge transistor gate capacitances
  Energy required to charge a capacitance, C, to VDD is CVDD2
  Circuit running at frequency f (f cycles per second)
  Capacitor is charged a times per cycle (discharging from 1 to 0 is free)
Dynamic power consumption:
Pdynamic = aCVDD2f
Dynamic Power Consumption

## Slide 91
a is the fraction of cycles that cap is charged
  Clock a = 1
  Data switching once per cycle a = 0.5
  Random data a = 0.25
  Typical data a = 0.1
Activty Factor a

## Slide 92
Power consumed when no gates are switching
Caused by the quiescent supply current, IDD (also called the leakage current)
Static power consumption:
Pstatic = IDDVDD
Static Power Consumption

## Slide 93
Chips have tiny capacitances, small currents, and high frequencies.
Units
Unit | Prefix | Value
Tera | T | 1012
Giga | G | 109
Mega | M | 106
Kilo | K | 103
Mili | m | 10-3
Micro | m | 10-6
Nano | n | 10-9
Pico | p | 10-12
Femto | f | 10-15

## Slide 94
Estimate the power consumption of a mobile phone running Angry Birds
  VDD = 0.8 V
  C = 5 nF
  f = 2 GHz
  a = 0.1
  IDD = 100 mA
P = aCVDD2f + IDDVDD
= (0.1)(5 nF)(0.8 V)2(2 GHz) + (100 mA)(0.8 V)
= (0.64 + 0.08) W ≈ 0.72 W
Power Consumption Example

## Slide 95
If the phone has a 8 W-hr battery, estimate its battery life sitting idle in your pocket.
  VDD = 0.8 V
  IDD = 100 mA
Pstatic = IDDVDD = 0.08 W
Battery life = Capacity / Consumption
= (8 W-hr) / (0.08 W) = 100 hr (4 days)
Power Consumption Example

## Slide 96
Digital Design and Computer Architecture Lecture Notes
© 2021 Sarah Harris and David Harris
These notes may be used and modified for educational and/or non-commercial purposes so long as the source is attributed.
About these Notes