## Slide 1
Chapter 6:
Architecture
Digital Design &
Computer Architecture
Sarah Harris & David Harris

## Slide 2
Chapter 6 :: Topics
Introduction
Assembly Language
Programming
Machine Language
Addressing Modes
Lights, Camera, Action: Compiling, Assembly, & Loading
Odds & Ends

## Slide 3
Introduction
Jumping up a few levels of abstraction
Architecture: programmer’s view of computer
  Defined by instructions & operand locations
Microarchitecture: how to implement an architecture in hardware (covered in Chapter 7)

## Slide 4
Assembly Language
Instructions: commands in a computer’s language
  Assembly language: human-readable format of instructions
  Machine language: computer-readable format (1’s and 0’s)
RISC-V architecture:
  Developed by Krste Asanovic, David Patterson and their colleagues at UC Berkeley in 2010.
  First widely accepted open-source computer architecture
Once you’ve learned one architecture, it’s easier to learn others

## Slide 5
Kriste Asanovic
Professor of Computer Science at the University of California, Berkeley
Developed RISC-V during one summer
Chairman of the Board of the RISC-V Foundation
Co-Founder of SiFive, a company that commercializes and develops supporting tools for RISC-V

## Slide 6
Andrew Waterman
Co-founded SiFive with Krste Asanovic
Weary of existing instruction set architectures (ISAs), he co-designed the RISC-V architecture and the first RISC-V cores
Earned his PhD in computer science from UC Berkeley in 2016

## Slide 7
David Patterson
Professor of Computer Science at the University of California, Berkeley since 1976
Coinvented the Reduced Instruction Set Computer (RISC) with John Hennessy in the 1980’s
Founding member of RISC-V team.
Was given the Turing Award (with John Hennessy) for pioneering a quantitative approach to the design and evaluation of computer architectures.

## Slide 8
John Hennessy
President of Stanford University from 2000 - 2016.
Professor of Electrical Engineering and Computer Science at Stanford since 1977
Coinvented the Reduced Instruction Set Computer (RISC) with David Patterson in the 1980’s
Was given the Turing Award (with David Patterson) for pioneering a quantitative approach to the design and evaluation of computer architectures.

## Slide 9
Architecture Design Principles
Underlying design principles, as articulated by Hennessy and Patterson:
    Simplicity favors regularity
    Make the common case fast
    Smaller is faster
    Good design demands good compromises

## Slide 10
Chapter 6: Architecture
Instructions

## Slide 11
Instructions: Addition
add: mnemonic indicates operation to perform
b, c: source operands (on which the operation is
performed)
a: destination operand (to which the result is
written)
C Code
a = b + c;
RISC-V assembly code
add a, b, c

## Slide 12
Instructions: Subtraction
Similar to addition - only mnemonic changes
sub: mnemonic
b, c: source operands
a: destination operand
C Code
a = b - c;
RISC-V assembly code
sub a, b, c

## Slide 13
Design Principle 1
Simplicity favors regularity
Consistent instruction format
Same number of operands (two sources and one destination)
Easier to encode and handle in hardware

## Slide 14
Multiple Instructions
More complex code is handled by multiple RISC-V instructions.
C Code
a = b + c - d;
RISC-V assembly code
add t, b, c # t = b + c
sub a, t, d # a = t - d

## Slide 15
Design Principle 2
Make the common case fast
RISC-V includes only simple, commonly used instructions
Hardware to decode and execute instructions can be simple, small, and fast
More complex instructions (that are less common) performed using multiple simple instructions
RISC-V is a reduced instruction set computer (RISC), with a small number of simple instructions
Other architectures, such as Intel’s x86, are complex instruction set computers (CISC)

## Slide 16
Chapter 6: Architecture
Operands

## Slide 17
Operands
Operand location: physical location in computer
  Registers
  Memory
  Constants (also called immediates)

## Slide 18
Operands: Registers
RISC-V has 32 32-bit registers
Registers are faster than memory
RISC-V called “32-bit architecture” because it operates on 32-bit data

## Slide 19
Design Principle 3
Smaller is Faster
RISC-V includes only a small number of registers

## Slide 20
RISC-V Register Set
Name | Register Number | Usage
zero | x0 | Constant value 0
ra | x1 | Return address
sp | x2 | Stack pointer
gp | x3 | Global pointer
tp | x4 | Thread pointer
t0-2 | x5-7 | Temporaries
s0/fp | x8 | Saved register / Frame pointer
s1 | x9 | Saved register
a0-1 | x10-11 | Function arguments / return values
a2-7 | x12-17 | Function arguments
s2-11 | x18-27 | Saved registers
t3-6 | x28-31 | Temporaries

## Slide 21
Operands: Registers
Registers:
  Can use either name (i.e., ra, zero) or x0, x1, etc.
  Using name is preferred
Registers used for specific purposes:
    zero always holds the constant value 0.
    the saved registers, s0-s11, used to hold variables
    the temporary registers, t0-t6, used to hold intermediate values during a larger computation
    Discuss others later

## Slide 22
Instructions with Registers
Revisit add instruction
C Code
a = b + c;
RISC-V assembly code
# s0 = a, s1 = b, s2 = c
add s0, s1, s2
# indicates a single-line comment

## Slide 23
Instructions with Constants
addi instruction
C Code
a = b + 6;
RISC-V assembly code
# s0 = a, s1 = b
addi s0, s1, 6

## Slide 24
Chapter 6: Architecture
Memory Operands

## Slide 25
Operands: Memory
Too much data to fit in only 32 registers
Store more data in memory
Memory is large, but slow
Commonly used variables kept in registers

## Slide 26
Memory
First, we’ll discuss word-addressable memory
Then we’ll discuss byte-addressable memory
RISC-V is byte-addressable

## Slide 27
Word-Addressable Memory
Each 32-bit data word has a unique address
RISC-V uses byte-addressable memory, which we’ll talk about next.

## Slide 28
Reading Word-Addressable Memory
Memory read called load
Mnemonic: load word (lw)
Format:
  lw t1, 5(s0)
lw destination, offset(base)
Address calculation:
  add base address (s0) to the offset (5)
  address = (s0 + 5)
Result:
  t1 holds the data value at address (s0 + 5)
Any register may be used as base address

## Slide 29
Reading Word-Addressable Memory
Example: read a word of data at memory address 1 into s3
  address = (0 + 1) = 1
  s3 = 0xF2F1AC07 after load
Assembly code
lw s3, 1(zero) # read memory word 1 into s3

## Slide 30
Writing Word-Addressable Memory
Memory write is called a store
Mnemonic: store word (sw)

## Slide 31
Writing Word-Addressable Memory
Example: Write (store) the value in t4 into memory address 3
  add the base address (zero) to the offset (0x3)
  address: (0 + 0x3) = 3
  for example, if t4 holds the value 0xFEEDCABB, then after this instruction completes, word 3 in memory will contain that value
Assembly code
sw t4, 0x3(zero) # write the value in t4
# to memory word 3
  Offset can be written in decimal (default) or hexadecimal

## Slide 32
Byte-Addressable Memory
Each data byte has a unique address
Load/store words or single bytes: load byte (lb) and store byte (sb)
32-bit word = 4 bytes, so word address increments by 4

## Slide 33
Reading Byte-Addressable Memory
The address of a memory word must now be multiplied by 4. For example,
  the address of memory word 2 is 2 × 4 = 8
  the address of memory word 10 is 10 × 4 = 40 (0x28)
RISC-V is byte-addressed, not word-addressed

## Slide 34
Reading Byte-Addressable Memory
Example: Load a word of data at memory address 8 into s3.
s3 holds the value 0x1EE2842 after load
RISC-V assembly code
lw s3, 8(zero) # read word at address 8 into s3

## Slide 35
Writing Byte-Addressable Memory
Example: store the value held in t7 into memory address 0x10 (16)
  if t7 holds the value 0xAABBCCDD, then after the sw completes, word 4 (at address 0x10) in memory will contain that value
RISC-V assembly code
sw t7, 0x10(zero) # write t7 into address 16

## Slide 36
Chapter 6: Architecture
Generating Constants

## Slide 37
Generating 12-Bit Constants
12-bit signed constants (immediates) using addi:
Any immediate that needs more than 12 bits cannot use this method.
C Code
// int is a 32-bit signed word
int a = -372;
int b = a + 6;
RISC-V assembly code
# s0 = a, s1 = b
addi s0, zero, -372
addi s1, s0, 6

## Slide 38
Generating 32-bit Constants
Use load upper immediate (lui) and addi
lui: puts an immediate in the upper 20 bits of destination register and 0’s in lower 12 bits
C Code
int a = 0xFEDC8765;
RISC-V assembly code
# s0 = a
lui s0, 0xFEDC8
addi s0, s0, 0x765
Remember that addi sign-extends its 12-bit immediate

## Slide 39
Generating 32-bit Constants
If bit 11 of 32-bit constant is 1, increment upper 20 bits by 1 in lui
C Code
int a = 0xFEDC8EAB;
RISC-V assembly code
# s0 = a
lui s0, 0xFEDC9 # s0 = 0xFEDC9000
addi s0, s0, -341 # s0 = 0xFEDC9000 + 0xFFFFFEAB
# = 0xFEDC8EAB
Note: -341 = 0xEAB

## Slide 40
Chapter 6: Architecture
Logical / Shift Instructions

## Slide 41
Programming
High-level languages:
  e.g., C, Java, Python
  Written at higher level of abstraction
High-level constructs: loops, conditional statements, arrays, function calls
First, introduce instructions that support these:
  Logical operations
  Shift instructions
  Multiplication & division
  Branches & Jumps

## Slide 42
Ada Lovelace, 1815-1852
Wrote the first computer program
Her program calculated the Bernoulli numbers on Charles Babbage’s Analytical Engine
She was the daughter of the poet Lord Byron

## Slide 43
Logical Instructions
and, or, xor
  and: useful for masking bits
    Masking all but the least significant byte of a value:
    0xF234012F AND 0x000000FF = 0x0000002F
  or: useful for combining bit fields
    Combine 0xF2340000 with 0x000012BC:
    0xF2340000 OR 0x000012BC = 0xF23412BC
  xor: useful for inverting bits:
    A XOR -1 = NOT A (remember that -1 = 0xFFFFFFFF)

## Slide 44
Logical Instructions: Example 1

## Slide 45
Logical Instructions: Example 2
-1484 = 0xA34 in 12-bit 2’s complement representation.

## Slide 46
Shift Instructions
Shift amount is in (lower 5 bits of) a register
sll: shift left logical
  Example: sll t0, t1, t2 # t0 = t1 << t2
srl: shift right logical
  Example: srl t0, t1, t2 # t0 = t1 >> t2
sra: shift right arithmetic
  Example: sra t0, t1, t2 # t0 = t1 >>> t2

## Slide 47
Immediate Shift Instructions
Shift amount is an immediate between 0 to 31
slli: shift left logical immediate
  Example: slli t0, t1, 23 # t0 = t1 << 23
srli: shift right logical immediate
  Example: srli t0, t1, 18 # t0 = t1 >> 18
srai: shift right arithmetic immediate
  Example: srai t0, t1, 5 # t0 = t1 >>> 5

## Slide 48
Chapter 6: Architecture
Multiplication and Division

## Slide 49
Multiplication
32 × 32 multiplication → 64 bit result
  mul s3, s1, s2
  s3 = lower 32 bits of result
  mulh s4, s1, s2
  s4 = upper 32 bits of result, treats operands as signed
  {s4, s3} = s1 x s2
Example: s1 = 0x40000000 = 230; s2 = 0x80000000 = -231
s1 x s2 = -261 = 0xE0000000 00000000
s4 = 0xE0000000; s3 = 0x00000000

## Slide 50
Division
32-bit division → 32-bit quotient & remainder
  div s3, s1, s2 # s3 = s1/s2
  rem s4, s1, s2 # s4 = s1%s2
Example: s1 = 0x00000011 = 17; s2 = 0x00000003 = 3
s1 / s2 = 5
s1 % s2 = 2
s3 = 0x00000005; s4 = 0x00000002

## Slide 51
Chapter 6: Architecture
Branches & Jumps

## Slide 52
Branching
Execute instructions out of sequence
Types of branches:
  Conditional
    branch if equal (beq)
    branch if not equal (bne)
    branch if less than (blt)
    branch if greater than or equal (bge)
  Unconditional
    jump (j)
    jump register (jr)
    jump and link (jal)
    jump and link register (jalr)
We’ll talk about these when discuss function calls

## Slide 53
Conditional Branching
# RISC-V assembly
addi s0, zero, 4 # s0 = 0 + 4 = 4
addi s1, zero, 1 # s1 = 0 + 1 = 1
slli s1, s1, 2 # s1 = 1 << 2 = 4
beq s0, s1, target # branch is taken
addi s1, s1, 1 # not executed
sub s1, s1, s0 # not executed
target: # label
add s1, s1, s0 # s1 = 4 + 4 = 8
Labels indicate instruction location. They can’t be reserved words and must be followed by a colon (:)

## Slide 54
The Branch Not Taken (bne)
# RISC-V assembly
addi s0, zero, 4 # s0 = 0 + 4 = 4
addi s1, zero, 1 # s1 = 0 + 1 = 1
slli s1, s1, 2 # s1 = 1 << 2 = 4
bne s0, s1, target # branch not taken
addi s1, s1, 1 # s1 = 4 + 1 = 5
sub s1, s1, s0 # s1 = 5 – 4 = 1
target:
add s1, s1, s0 # s1 = 1 + 4 = 5

## Slide 55
Unconditional Branching (j)
# RISC-V assembly
j target # jump to target
srai s1, s1, 2 # not executed
addi s1, s1, 1 # not executed
sub s1, s1, s0 # not executed
target:
add s1, s1, s0 # s1 = 1 + 4 = 5

## Slide 56
Chapter 6: Architecture
Conditional
Statements & Loops

## Slide 57
Conditional Statements & Loops
Conditional Statements
  if statements
  if/else statements
Loops
  while loops
  for loops

## Slide 58
If Statement
C Code
if (i == j)
f = g + h;
f = f – i;
RISC-V assembly code
# s0 = f, s1 = g, s2 = h
# s3 = i, s4 = j
bne s3, s4, L1
add s0, s1, s2
L1:
sub s0, s0, s3
Assembly tests opposite case (i != j) of high-level code (i == j)

## Slide 59
If/Else Statement
C Code
if (i == j)
f = g + h;
else
f = f – i;
RISC-V assembly code
# s0 = f, s1 = g, s2 = h
# s3 = i, s4 = j
bne s3, s4, L1
add s0, s1, s2
j done
L1:
sub s0, s0, s3
done:
Assembly tests opposite case (i != j) of high-level code (i == j)

## Slide 60
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
RISC-V assembly code
# s0 = pow, s1 = x
addi s0, zero, 1
add s1, zero, zero
addi t0, zero, 128
while:
beq s0, t0, done
slli s0, s0, 1
addi s1, s1, 1
j while
done:
While Loops
Assembly tests opposite case (pow == 128) of high-level code ( pow != 128)

## Slide 61
For Loops
for (initialization; condition; loop operation)
statement
initialization: executes before the loop begins
condition: is tested at the beginning of each iteration
loop operation: executes at the end of each iteration
statement: executes each time the condition is met

## Slide 62
For Loops
C Code
// add the numbers from 0 to 9
int sum = 0;
int i;
for (i=0; i!=10; i = i+1) {
sum = sum + i;
}
RISC-V assembly code
# s0 = i, s1 = sum
addi s1, zero, 0
add s0, zero, zero
addi t0, zero, 10
for:
beq s0, t0, done
add s1, s1, s0
addi s0, s0, 1
j for
done:

## Slide 63
Less Than Comparison
C Code
// add the powers of 2 from 1
// to 100
int sum = 0;
int i;
for (i=1; i < 101; i = i*2) {
sum = sum + i;
}
RISC-V assembly code
# s0 = i, s1 = sum
addi s1, zero, 0
addi s0, zero, 1
addi t0, zero, 101
loop:
bge s0, t0, done
add s1, s1, s0
slli s0, s0, 1
j loop
done:

## Slide 64
Less Than Comparison: Version 2
C Code
// add the powers of 2 from 1
// to 100
int sum = 0;
int i;
for (i=1; i < 101; i = i*2) {
sum = sum + i;
}
RISC-V assembly code
# s0 = i, s1 = sum
addi s1, zero, 0
addi s0, zero, 1
addi t0, zero, 101
loop:
slt t2, s0, t0
beq t2, zero, done
add s1, s1, s0
slli s0, s0, 1
j loop
done:
slt: set if less than instruction
slt t2, s0, t0 # if s0 < t0, t2 = 1
# otherwise t2 = 0

## Slide 65
Chapter 6: Architecture
Arrays

## Slide 66
Arrays
Access large amounts of similar data
Index: access each element
Size: number of elements

## Slide 67
Arrays
5-element array
Base address = 0x123B4780 (address of first element, array[0])
First step in accessing an array: load base address into a register

## Slide 68
Accessing Arrays
// C Code
int array[5];
array[0] = array[0] * 2;
array[1] = array[1] * 2;
# RISC-V assembly code
# s0 = array base address
lui s0, 0x123B4 # 0x123B4 in upper 20 bits of s0
addi s0, s0, 0x780 # s0 = 0x123B4780
lw t1, 0(s0) # t1 = array[0]
slli t1, t1, 1 # t1 = t1 * 2
sw t1, 0(s0) # array[0] = t1
lw t1, 4(s0) # t1 = array[1]
slli t1, t1, 1 # t1 = t1 * 2
sw t1, 4(s0) # array[1] = t1

## Slide 69
Accessing Arrays Using For Loops
// C Code
int array[1000];
int i;
for (i=0; i < 1000; i = i + 1)
array[i] = array[i] * 8;
# RISC-V assembly code
# s0 = array base address, s1 = i

## Slide 70
Accessing Arrays Using For Loops
# RISC-V assembly code
# s0 = array base address, s1 = i
# initialization code
lui s0, 0x23B8F # s0 = 0x23B8F000
ori s0, s0, 0x400 # s0 = 0x23B8F400
addi s1, zero, 0 # i = 0
addi t2, zero, 1000 # t2 = 1000
loop:
bge s1, t2, done # if not then done
slli t0, s1, 2 # t0 = i * 4 (byte offset)
add t0, t0, s0 # address of array[i]
lw t1, 0(t0) # t1 = array[i]
slli t1, t1, 3 # t1 = array[i] * 8
sw t1, 0(t0) # array[i] = array[i] * 8
addi s1, s1, 1 # i = i + 1
j loop # repeat
done:

## Slide 71
ASCII Code
ASCII: American Standard Code for Information Interchange
Each text character has unique byte value
  For example, S = 0x53, a = 0x61, A = 0x41
  Lower-case and upper-case differ by 0x20 (32)

## Slide 72
Cast of Characters: ASCII Encodings
# | Char | # | Char | # | Char | # | Char | # | Char | # | Char
20 | space | 30 | 0 | 40 | @ | 50 | P | 60 | ` | 70 | p
21 | ! | 31 | 1 | 41 | A | 51 | Q | 61 | a | 71 | q
22 | “ | 32 | 2 | 42 | B | 52 | R | 62 | b | 72 | r
23 | # | 33 | 3 | 43 | C | 53 | S | 63 | c | 73 | s
24 | $ | 34 | 4 | 44 | D | 54 | T | 64 | d | 74 | t
25 | % | 35 | 5 | 45 | E | 55 | U | 65 | e | 75 | u
26 | & | 36 | 6 | 46 | F | 56 | V | 66 | f | 76 | v
27 | ‘ | 37 | 7 | 47 | G | 57 | W | 67 | g | 77 | w
28 | ( | 38 | 8 | 48 | H | 58 | X | 68 | h | 78 | x
29 | ) | 39 | 9 | 49 | I | 59 | Y | 69 | i | 79 | y
2A | * | 3A | : | 4A | J | 5A | Z | 6A | j | 7A | z
2B | + | 3B | ; | 4B | K | 5B | [ | 6B | k | 7B | {
2C | , | 3C | < | 4C | L | 5C | \ | 6C | l | 7C | ¦
2D | - | 3D | = | 4D | M | 5D | ] | 6D | m | 7D | }
2E | . | 3E | > | 4E | N | 5E | ^ | 6E | n | 7E | ~
2F | / | 3F | ? | 4F | O | 5F | _ | 6F | o |  | 

## Slide 73
Accessing Arrays of Characters
// C Code
char str[80] = “CAT”;
int len = 0;
// compute length of string
while (str[len]) len++;
# RISC-V assembly code
# s0 = array base address, s1 = len
addi s1, zero, 0 # len = 0
while: add t0, s0, s1 # address of str[len]
lw t1, 0(t0) # load str[len]
beq t1, zero, done # are we at the end of the string?
addi s1, s1, 1 # len++
j while # repeat while loop
done:

## Slide 74
Chapter 6: Architecture
Function Calls

## Slide 75
Function Calls
Caller: calling function (in this case, main)
Callee: called function (in this case, sum)
C Code
void main()
{
int y;
y = sum(42, 7);
...
}
int sum(int a, int b)
{
return (a + b);
}

## Slide 76
Simple Function Call
void means that simple doesn’t return a value
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
RISC-V assembly code
0x00000300 main: jal simple # call
0x00000304 add s0, s1, s2
... ...
0x0000051c simple: jr ra # return
jal simple:
ra = PC + 4 (0x00000304)
jumps to simple label (PC = 0x0000051c)
jr ra:
PC = ra (0x00000304)

## Slide 77
Function Calling Conventions
Caller:
  passes arguments to callee
  jumps to callee
Callee:
  performs the function
  returns result to caller
  returns to point of call
  must not overwrite registers or memory needed by caller

## Slide 78
RISC-V Function Calling Conventions
Call Function: jump and link (jal func)
Return from function: jump register (jr ra)
Arguments: a0 – a7
Return value: a0

## Slide 79
Input Arguments & Return Value
C Code
int main()
{
int y;
...
y = diffofsums(2, 3, 4, 5); // 4 arguments
...
}
int diffofsums(int f, int g, int h, int i)
{
int result;
result = (f + g) - (h + i);
return result; // return value
}

## Slide 80
Input Arguments & Return Value
RISC-V assembly code
# s7 = y
main:
. . .
addi a0, zero, 2 # argument 0 = 2
addi a1, zero, 3 # argument 1 = 3
addi a2, zero, 4 # argument 2 = 4
addi a3, zero, 5 # argument 3 = 5
jal diffofsums # call function
add s7, a0, zero # y = returned value
. . .
# s3 = result
diffofsums:
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
jr ra # return to caller

## Slide 81
Input Arguments & Return Value
RISC-V assembly code
# s3 = result
diffofsums:
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
jr ra # return to caller
diffofsums overwrote 3 registers: t0, t1, s3
diffofsums can use stack to temporarily store registers

## Slide 82
Chapter 6: Architecture
The Stack

## Slide 83
The Stack
Memory used to temporarily save variables
Like stack of dishes, last-in-first-out (LIFO) queue
Expands: uses more memory when more space needed
Contracts: uses less memory when the space is no longer needed

## Slide 84
The Stack
Grows down (from higher to lower memory addresses)
Stack pointer: sp points to top of the stack
Make room on stack for 2 words.

## Slide 85
How Functions use the Stack
Called functions must have no unintended side effects
But diffofsums overwrites 3 registers: t0, t1, s3
# RISC-V assembly
# s3 = result
diffofsums:
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
jr ra # return to caller

## Slide 86
Storing Register Values on the Stack
# s3 = result
diffofsums:
addi sp, sp, -12 # make space on stack to
# store three registers
sw s3, 8(sp) # save s3 on stack
sw t0, 4(sp) # save t0 on stack
sw t1, 0(sp) # save t1 on stack
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
lw s3, 8(sp) # restore s3 from stack
lw t0, 4(sp) # restore t0 from stack
lw t1, 0(sp) # restore t1 from stack
addi sp, sp, 12 # deallocate stack space
jr ra # return to caller

## Slide 87
The Stack During diffofsums Call

## Slide 88
Preserved Registers
Preserved Callee-Saved | Nonpreserved Caller-Saved
s0-s11 | t0-t6
sp | a0-a7
ra | 
stack above sp | stack below sp

## Slide 89
Storing Saved Registers on the Stack
# s3 = result
diffofsums:
addi sp, sp, -4 # make space on stack to
# store one register
sw s3, 0(sp) # save s3 on stack
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub s3, t0, t1 # result = (f + g) − (h + i)
add a0, s3, zero # put return value in a0
lw s3, 0(sp) # restore s3 from stack
addi sp, sp, 4 # deallocate stack space
jr ra # return to caller

## Slide 90
Optimized diffofsums
# a0 = result
diffofsums:
add t0, a0, a1 # t0 = f + g
add t1, a2, a3 # t1 = h + i
sub a0, t0, t1 # result = (f + g) − (h + i)
jr ra # return to caller

## Slide 91
Non-Leaf Function Calls
Non-leaf function:
a function that calls another function
func1:
addi sp, sp, -4 # make space on stack
sw ra, 0(sp) # save ra on stack
jal func2
...
lw ra, 0(sp) # restore ra from stack
addi sp, sp, 4 # deallocate stack space
jr ra # return to caller
Must preserve ra before function call.

## Slide 92
Non-Leaf Function Call Example
# f1 (non-leaf function) uses s4-s5 and needs a0-a1 after call to f2
f1:
addi sp, sp, -20 # make space on stack for 5 words
sw a0, 16(sp)
sw a1, 12(sp)
sw ra, 8(sp) # save ra on stack
sw s4, 4(sp)
sw s5, 0(sp)
jal func2
...
lw ra, 8(sp) # restore ra (and other regs) from stack
...
addi sp, sp, 20 # deallocate stack space
jr ra # return to caller
# f2 (leaf function) only uses s4 and calls no functions
f2:
addi sp, sp, -4 # make space on stack for 1 word
sw s4, 0(sp)
...
lw s4, 0(sp)
addi sp, sp, 4 # deallocate stack space
jr ra # return to caller

## Slide 93
Stack during Function Calls

## Slide 94
Function Call Summary
Caller
  Save any needed registers (ra, maybe t0-t6/a0-a7)
  Put arguments in a0-a7
  Call function: jal callee
  Look for result in a0
  Restore any saved registers
Callee
  Save registers that might be disturbed (s0-s11)
  Perform function
  Put result in a0
  Restore registers
  Return: jr ra

## Slide 95
Chapter 6: Architecture
Recursive Functions

## Slide 96
Recursive Function Example
Function that calls itself
When converting to assembly code:
  In the first pass, treat recursive calls as if it’s calling a different function and ignore overwritten registers.
  Then save/restore registers on stack as needed.

## Slide 97
Recursive Function Example
Factorial function:
  factorial(n) = n!
  = n*(n-1)*(n-2)*(n-3)…*1
  Example: factorial(6) = 6!
  = 6*5*4*3*2*1
  = 720

## Slide 98
Recursive Function Example
  High-Level Code
  int factorial(int n) {
  if (n <= 1)
  return 1;
  else
  return (n*factorial(n−1));
  }
  Example: n = 3
  factorial(3): returns 3*factorial(2)
  factorial(2): returns 2*factorial(1)
  factorial(1): returns 1
  Thus,
  factorial(1): returns 1
  factorial(2): returns 2*1 = 2
  factorial(3): returns 3*2 = 6

## Slide 99
Recursive Function Example
  High-Level Code
  int factorial(int n) {
  if (n <= 1)
  return 1;
  else
  return (n*factorial(n−1));
  }
  RISC-V Assembly
  factorial:
  addi t0, zero, 1 # temporary = 1
  bgt a0, t0, else # if n>1, go to else
  addi a0, zero, 1 # otherwise, return 1
  jr ra # return
  else:
  addi a0, a0, -1 # n = n − 1
  jal factorial # recursive call
  mul a0, a0, a0 # a0=n*factorial(n−1)
  jr ra # return
  Pass 1. Treat as if calling another function. Ignore stack.
  Pass 2. Save overwritten registers (needed after function call) on the stack before call.
Problem: n (a0) was overwritten by function call!
Must save it (and ra) on stack before function call.
n
return value: factorial(n-1)

## Slide 100
Recursive Function Example
  High-Level Code
  int factorial(int n) {
  if (n <= 1)
  return 1;
  else
  return (n*factorial(n−1));
  }
  RISC-V Assembly
  factorial:
  addi sp, sp, -8 # save regs
  sw a0, 4(sp)
  sw ra, 0(sp)
  addi t0, zero, 1 # temporary = 1
  bgt a0, t0, else # if n>1, go to else
  addi a0, zero, 1 # otherwise, return 1
  addi sp, sp, 8 # restore sp
  jr ra # return
  else:
  addi a0, a0, -1 # n = n − 1
  jal factorial # recursive call
  lw t1, 4(sp) # restore n into t1
  lw ra, 0(sp) # restore ra
  addi sp, sp, 8 # restore sp
  mul a0, t1, a0 # a0=n*factorial(n−1)
  jr ra # return
  Pass 1. Treat as if calling another function. Ignore stack.
  Pass 2. Save overwritten registers (needed after function call) on the stack before call.
Note: n is restored from stack into t1 so it doesn’t overwrite return value in a0.

## Slide 101
Recursive Functions
  0x8500 factorial: addi sp, sp, -8 # save registers
  0x8504 sw a0, 4(sp)
  0x8508 sw ra, 0(sp)
  0x850C addi t0, zero, 1 # temporary = 1
  0x8510 bgt a0, t0, else # if n > 1, go to else
  0x8514 addi a0, zero, 1 # otherwise, return 1
  0x8518 addi sp, sp, 8 # restore sp
  0x851C jr ra # return
  0x8520 else: addi a0, a0, -1 # n = n − 1
  0x8524 jal factorial # recursive call
  0x8528 lw t1, 4(sp) # restore n into t1
  0x852C lw ra, 0(sp) # restore ra
  0x8530 addi sp, sp, 8 # restore sp
  0x8534 mul a0, t1, a0 # a0 = n*factorial(n−1)
  0x8538 jr ra # return
  PC+4 = 0x8528 when factorial is called recursively.

## Slide 102
Stack During Recursive Function
When factorial(3) is called:

## Slide 103
Chapter 6: Architecture
More on Jumps & Pseudoinstructions

## Slide 104
Jumps
RISC-V has two types of unconditional jumps
  Jump and link (jal rd, imm20:0)
    rd = PC+4; PC = PC + imm
  jump and link register (jalr rd, rs, imm11:0)
    rd = PC+4; PC = [rs] + SignExt(imm)

## Slide 105
Pseudoinstructions
Pseudoinstructions are not actual RISC-V instructions but they are often more convenient for the programmer.
Assembler converts them to real RISC-V instructions.

## Slide 106
Jump Pseudoinstructions
RISC-V has four jump psuedoinstructions
  j imm jal x0, imm
  jal imm jal ra, imm
  jr rs jalr x0, rs, 0
  ret jr ra (i.e., jalr x0, ra, 0)

## Slide 107
Labels
Label indicates where to jump
Represented in jump as immediate offset
  imm = # bytes past jump instruction
  In example, below, imm = (51C-300) = 0x21C
  jal simple = jal ra, 0x21C
RISC-V assembly code
0x00000300 main: jal simple # call
0x00000304 add s0, s1, s1
... ...
0x0000051c simple: jr ra # return

## Slide 108
Long Jumps
The immediate is limited in size
  20 bits for jal, 12 bits for jalr
  Limits how far a program can jump
Special instruction to help jumping further
  auipc rd, imm: add upper immediate to PC
    rd = PC + {imm31:12, 12’b0}
Pseudoinstruction: call imm31:0
  Behaves like jal imm, but allows 32-bit immediate offset
    auipc ra, imm31:12
    jalr ra, ra, imm11:0

## Slide 109
More RISC-V Pseudoinstructions
See Appendix B for more pseudoinstructions.
Pseudoinstruction | RISC-V Instructions
j label | jal zero, label
jr ra | jalr zero, ra, 0
mv t5, s3 | addi t5, s3, 0
not s7, t2 | xori s7, t2, -1
nop | addi zero, zero, 0
li s8, 0x56789DEF | lui s8, 0x5678A addi s8, s8, 0xDEF
bgt s1, t3, L3 | blt t3, s1, L3
bgez t2, L7 | bge t2, zero, L7
call L1 | auipc ra, imm31:12 jalr ra, ra, imm11:0
ret | jalr zero, ra, 0

## Slide 110
Chapter 6: Architecture
Machine Language

## Slide 111
Machine Language
Binary representation of instructions
Computers only understand 1’s and 0’s
32-bit instructions
  Simplicity favors regularity: 32-bit data & instructions
4 Types of Instruction Formats:
  R-Type
  I-Type
  S/B-Type
  U/J-Type

## Slide 112
R-Type
Register-type
3 register operands:
  rs1, rs2: source registers
  rd: destination register
Other fields:
  op: the operation code or opcode
  funct7,funct3:
  the function (7 bits and 3-bits, respectively)
  with opcode, tells computer what operation to perform

## Slide 113
R-Type Examples

## Slide 114
Chapter 6: Architecture
Machine Language:
More Formats

## Slide 115
I-Type
Immediate-type
3 operands:
  rs1: register source operand
  rd: register destination operand
  imm: 12-bit two’s complement immediate
Other fields:
  op: the opcode
    Simplicity favors regularity: all instructions have opcode
  funct3: the function (3-bit function code)
    with opcode, tells computer what operation to perform

## Slide 116
I-Type Examples

## Slide 117
S/B-Type
Store-Type
Branch-Type
Differ only in immediate encoding

## Slide 118
S-Type
Store-Type
3 operands:
  rs1: base register
  rs2: value to be stored to memory
  imm: 12-bit two’s complement immediate
Other fields:
  op: the opcode
    Simplicity favors regularity: all instructions have opcode
  funct3: the function (3-bit function code)
    with opcode, tells computer what operation to perform

## Slide 119
S-Type Examples

## Slide 120
B-Type
Branch-Type (similar format to S-Type)
3 operands:
  rs1: register source 1
  rs2: register source 2
  imm12:1: 12-bit two’s complement immediate – address offset
Other fields:
  op: the opcode
    Simplicity favors regularity: all instructions have opcode
  funct3: the function (3-bit function code)
    with opcode, tells computer what operation to perform

## Slide 121
B-Type Example
The 13-bit immediate encodes where to branch (relative to the branch instruction)
Immediate encoding is strange
Example:

## Slide 122
U/J-Type
Upper-Immediate-Type
Jump-Type
Differ only in immediate encoding

## Slide 123
U-Type
Upper-immediate-Type
Used for load upper immediate (lui)
2 operands:
  rd: destination register
  imm31:12:upper 20 bits of a 32-bit immediate
Other fields:
  op: the operation code or opcode – tells computer what
  operation to perform

## Slide 124
U-Type Example
Upper-immediate-Type
Used for load upper immediate (lui)
2 operands:
  rd: destination register
  imm31:12:upper 20 bits of a 32-bit immediate
Other fields:
  op: the operation code or opcode – tells computer what
  operation to perform

## Slide 125
J-Type
Jump-Type
Used for jump-and-link instruction (jal)
2 operands:
  rd: destination register
  imm20,10:1,11,19:12: 20 bits (20:1) of a 21-bit immediate
Other fields:
  op: the operation code or opcode – tells computer what
  operation to perform
Note: jalr is I-type, not j-type, to specify rs1

## Slide 126
J-Type Example
0xABC04 – 0x540C =
0XA67F8

## Slide 127
Review: Instruction Formats

## Slide 128
Design Principle 4
Good design demands good compromises
Multiple instruction formats allow flexibility
  add, sub: use 3 register operands
  lw, sw, addi: use 2 register operands and a constant
Number of instruction formats kept small
  to adhere to design principles 1 and 3 (simplicity favors regularity and smaller is faster).

## Slide 129
Chapter 6: Architecture
Immediate Encodings

## Slide 130
Constants / Immediates
lw and sw use constants or immediates
immediately available from instruction
12-bit two’s complement number
addi: add immediate
Is subtract immediate (subi) necessary?
C Code
a = a + 4;
b = a – 12;
RISC-V assembly code
# s0 = a, s1 = b
addi s0, s0, 4
addi s1, s0, -12

## Slide 131
Constants / Immediates
Immediate Bits

## Slide 132
Immediate Encodings
Immediate bits mostly occupy consistent instruction bits.
  Simplifies hardware to build the microprocessor
Sign bit of signed immediate is in msb of instruction.
Recall that rs2 of R-type can encode immediate shift amount.
Instruction Bits

## Slide 133
Composition of 32-bit Immediates
Immediate Bits
Instruction Bits

## Slide 134
Chapter 6: Architecture
Reading
Machine Language & Addressing Operands

## Slide 135
Instruction Fields & Formats
Instruction | op | funct3 | Funct7 | Type
add | 0110011 (51) | 000 (0) | 0000000 (0) | R-Type
sub | 0110011 (51) | 000 (0) | 0100000 (32) | R-Type
and | 0110011 (51) | 111 (7) | 0000000 (0) | R-Type
or | 0110011 (51) | 110 (6) | 0000000 (0) | R-Type
addi | 0010011 (19) | 000 (0) | - | I-Type
beq | 1100011 (99) | 000 (0) | - | B-Type
bne | 1100011 (99) | 001 (1) | - | B-Type
lw | 0000011 (3) | 010 (2) | - | I-Type
sw | 0100011 (35) | 010 (2) | - | S-Type
jal | 1101111 (111) | - | - | J-Type
jalr | 1100111 (103) | 000 (0) | - | I-Type
lui | 0110111 (55) | - | - | U-Type
See Appendix B for other instruction encodings

## Slide 136
Interpreting Machine Code
Write in binary
Start with op: tells how to parse rest
Extract fields
op, funct3, and funct7 fields tell operation
Ex: 0x41FE83B3 and 0xFDA58393
0x41FE83B3: 0100 0001 1111 1110 1000 0011 1011 0011
op = 51, funct3 = 0: add or sub (R-type)
funct7 = 0100000: sub
0xFDA48393: 1111 1101 1010 0100 1000 0011 1001 0011
op = 19, funct3 = 0: addi (I-type)

## Slide 137
Interpreting Machine Code
Write in binary
Start with op: tells how to parse rest
Extract fields
op, funct3, and funct7 fields tell operation
Ex: 0x41FE83B3 and 0xFDA58393

## Slide 138
Addressing Modes
How do we address the operands?
Register Only
Immediate
Base Addressing
PC-Relative

## Slide 139
Addressing Modes
Register Only
Operands found in registers
  Example: add s0, t2, t3
  Example: sub t6, s1, 0
Immediate
12-bit signed immediate used as an operand
  Example: addi s4, t5, -73
  Example: ori t3, t7, 0xFF

## Slide 140
Addressing Modes
Base Addressing
Loads and Stores
Address of operand is:
  base address + immediate
  Example: lw s4, 72(zero)
    address = 0 + 72
  Example: sw t2, -25(t1)
    address = t1 - 25

## Slide 141
Addressing Modes
PC-Relative Addressing: branches and jal
Example:
Address Instruction
0x354 L1: addi s1, s1, 1
0x358 sub t0, t1, s7
... ...
0xEB0 bne s8, s9, L1
  The label is (0xEB0-0x354) = 0xB5C (2908) instructions before bne

## Slide 142
Chapter 6: Architecture
Compiling, Assembling, & Loading Programs

## Slide 143
The Power of the Stored Program
32-bit instructions & data stored in memory
Sequence of instructions: only difference between two applications
To run a new program:
  No rewiring required
  Simply store new program in memory
Program Execution:
  Processor fetches (reads) instructions from memory in sequence
  Processor performs the specified operation

## Slide 144
The Stored Program
Program Counter (PC): keeps track of current instruction

## Slide 145
Alan Turing, 1912 - 1954
British mathematician and computer scientist
Founder of theoretical computer science
Invented the Turing machine: a mathematical model of computation
Designed the Automatic Computing Engine, one of first stored program computers
In 1952, was prosecuted for homosexual acts. Two years later, he died of cyanide poisoning.
The Turing Award was named in his honor, which is the highest honor in computing.

## Slide 146
How to Compile & Run a Program

## Slide 147
Grace Hopper, 1906 - 1992
Graduated from Yale University with a Ph.D. in mathematics
Developed first compiler
Helped develop the COBOL programming language
Highly awarded naval officer
Received World War II Victory Medal and National Defense Service Medal, among others

## Slide 148
What is Stored in Memory?
Instructions (also called text)
Data
  Global/static: allocated before program begins
  Dynamic: allocated within program
How big is memory?
  At most 232 = 4 gigabytes (4 GB)
  From address 0x00000000 to 0xFFFFFFFF

## Slide 149
Example RISC-V Memory Map

## Slide 150
Example Program: C Code
int f, g, y; // global variables
int func(int a, int b) {
if (b < 0)
return (a + b);
else
return(a + func(a, b-1));
}
void main() {
f = 2;
g = 3;
y = func(f,g);
return;
}

## Slide 151
Example Program: RISC-V Assembly
10144: ff010113 func: addi sp,sp,-16
10148: 00112623 sw ra,12(sp)
1014c: 00812423 sw s0,8(sp)
10150: 00050413 mv s0,a0
10154: 00a58533 add a0,a1,a0
10158: 0005da63 bgez a1,1016c <func+0x28>
1015c: 00c12083 lw ra,12(sp)
10160: 00812403 lw s0,8(sp)
10164: 01010113 addi sp,sp,16
10168: 00008067 ret
1016c: fff58593 addi a1,a1,-1
10170: 00040513 mv a0,s0
10174: fd1ff0ef jal ra,10144 <func>
10178: 00850533 add a0,a0,s0
1017c: fe1ff06f j 1015c <func+0x18>
Address Machine Code RISC-V Assembly Code
Maintain 4-word alignment of sp (for compatibility with RV128I) even though only space for 2 words needed.
Pseudoinstructions:
mv: addi a0, s0, 0
ret (return): jr ra

## Slide 152
Example Program: RISC-V Assembly
10180: ff010113 main: addi sp,sp,-16
10184: 00112623 sw ra,12(sp)
10188: 00200713 li a4,2
1018c: c4e1a823 sw a4,-944(gp) # 11a30 <f>
10190: 00300713 li a4,3
10194: c4e1aa23 sw a4,-940(gp) # 11a34 <g>
10198: 00300593 li a1,3
1019c: 00200513 li a0,2
101a0: fa5ff0ef jal ra,10144 <func>
101a4: c4a1ac23 sw a0,-936(gp) # 11a38 <y>
101a8: 00c12083 lw ra,12(sp)
101ac: 01010113 addi sp,sp,16
101b0: 00008067 ret
Address Machine Code RISC-V Assembly Code
gp = 0x11DE0
Put 2 and 3 in f and g (and argument registers) and call func. Then put result in y and return.

## Slide 153
Example Program: Symbol Table
text segment: address 0x10074
data segment: address 0x115e0
func function: address 0x10144 (size 0x3c bytes)
main function: address 0x10180 (size 0x34 bytes)
f: address 0x11a30 (size 0x4 bytes)
g: address 0x11a34 (size 0x4 bytes)
y: address 0x11a38 (size 0x4 bytes)
Address Size Symbol Name
00010074 l d .text 00000000 .text
000115e0 l d .data 00000000 .data
00010144 g F .text 0000003c func
00010180 g F .text 00000034 main
00011a30 g O .bss 00000004 f
00011a34 g O .bss 00000004 g
00011a38 g O .bss 00000004 y

## Slide 154
Example Program in Memory
Address of main:
0x10180

## Slide 155
Chapter 6: Architecture
Endianness

## Slide 156
Big-Endian & Little-Endian Memory
How to number bytes within a word?
Little-endian: byte numbers start at the little (least significant) end
Big-endian: byte numbers start at the big (most significant) end
Word address is the same for big- or little-endian

## Slide 157
Big-Endian & Little-Endian Memory
Jonathan Swift’s Gulliver’s Travels: the Little-Endians broke their eggs on the little end of the egg and the Big-Endians broke their eggs on the big end
It doesn’t really matter which addressing type used – except when the two systems need to share data!

## Slide 158
Big-Endian & Little-Endian Example
Suppose t0 initially contains 0x23456789
After following code runs on big-endian system, what value is s0?
In a little-endian system?
sw t0, 0(zero)
lb s0, 1(zero)
Big-endian: s0 = 0x00000045
Little-endian: s0 = 0x00000067

## Slide 159
Chapter 6: Architecture
Signed & Unsigned Instructions

## Slide 160
Signed & Unsigned Instructions
Multiplication and division
Branches
Set less than
Loads
Detecting overflow

## Slide 161
Multiplication
Signed: mulh
Unsigned: mulhu, mulhsu
  mulhu: treat both operands as unsigned
  mulhsu: treat first operand as signed, second as unsigned
  32 lsbs are identical whether signed/unsigned; use mul
Example: s1 = 0x80000000; s2 = 0xC0000000
mulh s4, s1, s2
mul s3, s1, s2
s1 = -231; s2 = -230
s1 x s2 = 261
s4 = 0x20000000
s3 = 0x00000000
mulhu s4, s1, s2
mul s3, s1, s2
s1 = 231; s2 = 3x230
s1 x s2 = 3x261
s4 = 0x60000000
s3 = 0x00000000
mulhsu s4, s1, s2
mul s3, s1, s2
s1 = -231; s2 = 3x230
s1 x s2 = -3x261
s4 = 0xA0000000
s3 = 0x00000000

## Slide 162
Division & Remainder
Signed: div, rem
Unsigned: divu, remu

## Slide 163
Branches
Signed: blt, bge
Unsigned: bltu, bgeu
Examples: s1 = 0x80000000; s2 = 0x40000000
blt s1, s2
s1 = -231; s2 = 230
taken
bltu s1, s2
s1 = 231; s2 = 230
not taken

## Slide 164
Set Less Than
Signed: slt, slti
Unsigned: sltu, sltiu
Note: RISC-V always sign-extends the immediate, even for sltiu
Examples: s1 = 0x80000000; s2 = 0x40000000
slt t0, s1, s2
s1 = -231; s2 = 230
t0 = 1
sltu t1, s1, s2
s1 = 231; s2 = 230
t1 = 0
slti t2, s1, -1 # -1 = 0xFFF
s1 = -231; imm = 0xFFFFFFFF = -1
t2 = 1
sltiu t3, s1, -1 # -1 = 0xFFF
s1 = 231; imm = 0xFFFFFFFF = 232 - 1
t3 = 1

## Slide 165
Loads
Signed:
  Sign-extends to create 32-bit value to load into register
  Load halfword: lh
  Load byte: lb
Unsigned:
  Zero-extends to create 32-bit value
  Load halfword unsigned: lhu
  Load byte: lbu

## Slide 166
Detecting Overflow
RISC-V does not provide unsigned addition or instructions or overflow detection because it can be done with existing instructions:
Example: Detecting unsigned overflow:
add t0, t1, t2
bltu t0, t1, overflow
Example: Detecting signed overflow:
add t0, t1, t2
slti t3, t2, 0 # t3=1 if t2 neg.
slt t4, t0, t1 # t4=1 if result < t1
bne t3, t4, overflow # overflow if:
# t2 neg & result>=t1 or
# t2 pos & result<t1

## Slide 167
Chapter 6: Architecture
Compressed Instructions

## Slide 168
Compressed Instructions
16-bit RISC-V instructions
Replace common integer and floating-point instructions with 16-bit versions.
Most RISC-V compilers/processors can use a mix of 32-bit and 16-bit instructions (and use 16-bit instructions whenever possible).
Uses prefix: c.
Examples:
  add → c.add
  lw → c.lw
  addi → c.addi

## Slide 169
Compressed Instructions Example
C Code
int i;
int scores[200];
for (i=0; i<200; i=i+1)
scores[i] = scores[i]+10;
RISC-V assembly code
# s0 = scores base address, s1 = i
c.li s1, 0 # i = 0
addi t2, zero, 200 # t2 = 200
for:
bge s1, t2, done # I >= 200? done
c.lw a3, 0(s0) # a3 = scores[i]
c.addi a3, 10 # a3 = scores[i]+10
c.sw a3, 0(s0) # scores[i] = a3
c.addi s0, 4 # next element
c.addi s1, 1 # i = i+1
c.j for # repeat
done:
200 is too big to fit in compressed immediate, so noncompressed addi used instead.
c.addi s0,4 is equivalent to addi s0,s0,4.
c.bge doesn’t exist, so bge is used.

## Slide 170
Compressed Machine Formats
Some compressed instructions use a 3-bit register code (instead of 5-bit). These specify registers x8 to x15.
Immediates are 6-11 bits.
Opcode is 2 bits.

## Slide 171
Compressed Machine Formats

## Slide 172
Chapter 6: Architecture
Floating-Point Instructions

## Slide 173
RISC-V Floating-Point Extensions
RISC-V offers three floating point extensions:
  RVF: single-precision (32-bit)
    8 exponent bits, 23 fraction bits
  RVD: double-precision (64-bit)
    11 exponent bits, 52 fraction bits
  RVQ: quad-precision (128-bit)
    15 exponent bits, 112 fraction bits

## Slide 174
Floating-Point Registers
32 Floating point registers
Width is highest precision – for example, if RVQ is implemented, registers are 128 bits wide
When multiple floating point extensions are implemented, the lower-precision values occupy the lower bits of the register

## Slide 175
Floating-Point Registers
Name | Register Number | Usage
ft0-7 | f0-7 | Temporary variables
fs0-1 | f8-9 | Saved variables
fa0-1 | f10-11 | Function arguments/Return values
fa2-7 | f12-17 | Function arguments
fs2-11 | f18-27 | Saved variables
ft8-11 | f28-31 | Temporary variables

## Slide 176
Floating-Point Instructions
Append .s (single), .d (double), .q (quad) for precision. I.e., fadd.s, fadd.d, and fadd.q
Arithmetic operations:
fadd, fsub, fdiv, fsqrt, fmin, fmax, multiply-add (fmadd, fmsub, fnmadd, fnmsub)
Other instructions:
move (fmv.x.w, fmv.w.x)
convert (fcvt.w.s, fcvt.s.w, etc.)
comparison (feq, flt, fle)
classify (fclass)
sign injection (fsgnj, fsgnjn, fsgnjx)
See Appendix B for additional RISC-V floating-point instructions.

## Slide 177
Floating-Point Multiply-Add
fmadd is the most critical instruction for signal processing programs.
Requires four registers.
fmadd.f f1, f2, f3, f4 # f1 = f2 x f3 + f4

## Slide 178
Floating-Point Example
RISC-V assembly code
# s0 = scores base address, s1 = i
addi s1, zero, 0 # i = 0
addi t2, zero, 200 # t2 = 200
addi t0, zero, 10 # ft0 = 10.0
fcvt.s.w ft0, t0
for:
bge s1, t2, done # i>=200? done
slli t0, s1, 2 # t0 = i*4
add t0, t0, s0 # scores[i] address
flw ft1, 0(t0) # ft1=scores[i]
fadd.s ft1, ft1, ft0 # ft1=scores[i]+10
fsw ft1, 0(t0) # scores[i] = t1
addi s1, s1, 1 # i = i+1
j for # repeat
done:
C Code
int i;
float scores[200];
for (i=0; i<200; i=i+1)
scores[i]=scores[i]+10;

## Slide 179
Floating-Point Instruction Formats
Use R-, I-, and S-type formats
Introduce another format for multiply-add instructions that have 4 register operands: R4-type

## Slide 180
Chapter 6: Architecture
Exceptions

## Slide 181
Exceptions
Unscheduled function call to exception handler
Caused by:
  Hardware, also called an interrupt, e.g., keyboard
  Software, also called traps, e.g., undefined instruction
When exception occurs, the processor:
  Records the cause of the exception
  Jumps to exception handler
  Returns to the program

## Slide 182
Exception Causes
Exception | Cause
Instruction address misaligned | 0
Instruction access fault | 1
Illegal instruction | 2
Breakpoint | 3
Load address misaligned | 4
Load access fault | 5
Store address misaligned | 6
Store access fault | 7
Environment call from U-Mode | 8
Environment call from S-Mode | 9
Environment call from M-Mode | 11

## Slide 183
RISC-V Privilege Levels
In RISC-V, exceptions occur at various privilege levels.
Privilege levels limit access to memory or certain (privileged) instructions.
RISC-V privilege modes are (from highest to lowest):
  Machine mode (bare metal)
  System mode (operating system)
  User mode (user program)
  Hypervisor mode (to support virtual machines)
For example, a program running in M-mode (machine mode) can access all memory or instructions – it has the highest privilege level.

## Slide 184
Exception Registers
Each privilege level has registers to handle exceptions
These registers are called control and status registers (CSRRs)
We discuss M-mode (machine mode) exceptions, but other modes are similar
M-mode registers used to handle exceptions are:
  mtvec, mcause, mepc, mscratch
(Likewise, S-mode exception registers are: stvec, scause, sepc, and mscratch; and so on for the other modes.)

## Slide 185
Exception Registers
CSRRs are not part of register file
M-mode CSRRs used to handle exceptions
  mtvec: holds address of exception handler code
  mcause: Records cause of exception
  mepc (Exception PC): Records PC where exception occurred
  mscratch: scratch space in memory for exception handlers

## Slide 186
Exception-Related Instructions
Called privileged instructions (because they access CSRRs)
  csrr: CSR register read
  csrw: CSR register write
  csrrw: CSR register read/write
  mret: returns to address held in mepc
Examples:
  csrr t1, mcause # t1 = mcause
  csrw mepc, t2 # mepc = t2
  cwrrw t0, mscratch, t1 # t0 = mscratch
  # mscratch = t1

## Slide 187
Exception Handler Summary
When a processor detects an exception:
  It jumps to exception handler address in mtvec
  The exception handler then:
    saves registers on small stack pointed to by mscratch
    Uses csrr (CSR read) to look at cause of exception (in mcause)
    Handles exception
    When finished, optionally increments mepc by 4 and restores registers from memory
    And then either aborts the program or returns to user code (using mret, which returns to address held in mepc)

## Slide 188
Example Exception Handler Code
Check for two types of exceptions:
  Illegal instruction (mcause = 2)
  Load address misaligned (mcause = 4)

## Slide 189
Example Exception Handler Code
# save registers that will be overwritten
csrrw t0, mscratch, t0 # swap t0 and mscratch
sw t1, 0(t0) # [mscratch] = t1
sw t2, 4(t0) # [mscratch+4] = t2
# check cause of exception
csrr t1, mcause # t1=mcause
addi t2, x0, 2 # t2=2 (illegal instruction exception code)
illegalinstr:
bne t1, t2, checkother # branch if not an illegal instruction
csrr t2, mepc # t2=exception PC
addi t2, t2, 4 # increment exception PC
csrw mepc, t2 # mepc=t2
j done # restore registers and return
checkother:
addi t2, x0, 4 # t2=4 (load address misaligned exception code)
bne t1, t2, done # branch if not a misaligned load
j exit # exit program
# restore registers and return from the exception
done:
lw t1, 0(t0) # t1 = [mscratch]
lw t2, 4(t0) # t2 = [mscratch+4]
csrrw t0, mscratch, t0 # swap t0 and mscratch
mret # return to program
exit:
...
Checks for two types of exceptions:
Illegal instruction (mcause = 2)
Load address misaligned (mcause = 4)

## Slide 190
Digital Design and Computer Architecture Lecture Notes
© 2021 Sarah Harris and David Harris
These notes may be used and modified for educational and/or non-commercial purposes so long as the source is attributed.
About these Notes